## Slide 1
Jeffery P. Hansen
Institute for Complex Engineered Systems
Carnegie Mellon University
October 26, 2005
Creating Virtual Peripheral Devices
in a Digital Circuit Simulator Using Tcl/Tk

## Slide 2: Outline
Overview of TkGate
Overview of Verilog
Virtual Peripheral Devices (VPDs)
VPD Tcl-Side
VPD Verilog-Side
Implementation
Conclusions

## Slide 3: TkGate 2.0 Overview
Interface Features
  Hybrid Tcl/Tk and Xlib/C based interface.
    Interface comprised of about 64K lines of C, 25K lines of Tcl/Tk.
    Separate simulator is about 31K lines of C.
  Multi-lingual interface with support for Catalan, English, French, German, Japanese, Spanish, Czech and Welsh.
  Design entry of both graphical and text/Verilog modules.
  User-defined device symbols.
  Support tools include a microcode/macrocode compiler.
Simulation Features
  Dynamically loadable Verilog scripts.
  Graphical display of simulation results.
  Breakpoints, single-step and clock-step simulator control.
  Interactive Virtual Peripheral Devices (VPD)
    Uses Tcl and Verilog to design interactive components.
    Tcl-Side and Verilog-side APIs facilitate communication.

## Slide 4: History of TkGate
Gate
Developed for Andrew Window Manager.
B/W Interface
Graphical Editor
Hierarchical Design
Custom Save Format
Used in Computer Arch. courses at CMU.
XGate
Ported to X11
Used in digital design and computer Arch. courses at CMU.
TkGate 0.1
Ported to Tcl/Tk
Verilog-like save file format.
“TTY” device.
TkGate 0.9
First public release.
TkGate 1.8.6
Current stable release
TkGate 2.0
Next planned release
Verilog-compliant save files.
Text Verilog Modules
Virtual Peripheral Devices
TTY and Drink Machine VPDs.
TkGate 1.8.0
Tcl/Tk 8.4 Compatibility
Redesigned Interface
1985
1990
1995
2000
2005
2010
TkGate 1.1
Color Interface

## Slide 5: TkGate Main Window
Memory Address Line
TTY Control Register
TTY Data Register
TTY Device
TTY Data/Control
Register Address

## Slide 6: Verilog
What is Verilog?
  Hardware description language used to describe hardware designs.
  Widely used industry standard for EDA (Electronic Design Automation) tools.
In what types of applications is Verilog used?
  Synthesis
  Simulation
  Formal verification
What do Verilog designs look like?
  Modular hierarchical design
  High degree of parallelism
  Multiple levels of abstraction including
    Structural – Module described as collection of connected blocks.
    Behavioral – Module described using C-like statements.

## Slide 7: Verilog Examples
module add(s,co,a,b,ci)
input a,b,ci;
output s,co;
xor g1 (w1,a,b);
xor g2 (s,w1,ci);
and g3 (w2,w1,ci);
and g4 (w3,a,b);
or g5 (co,w2,w3);
endmodule
g3
g1
g2
g5
g4
a
b
ci
s
co
w1
w2
w3
Structural Verilog
Behavioral Verilog
module count(state,ck,clr);
output [3:0] state;
reg [3:0] state;
input ck,clr;
initial
state = 4’h0;
always @(posedge ck)
state = state + 4’h1;
always @(clr)
if (clr)
state = 4’h0;
endmodule

## Slide 8: Verilog Design Hierarchy
module top;
foo f1;
foo f2;
endmodule
module foo;
bar b1;
zonk z1;
endmodule
module bar;
endmodule
module zonk;
bar bz;
endmodule
top
foo
foo
bar
zonk
bar
zonk
bar
bar
top.f1
top.f2
top.f1.b1
top.f1.z1
top.f2.z1
top.f2.b1
top.f1.z1.bz
top.f2.z1.bz
top

## Slide 9: TTY Virtual Peripheral Device
main.mem
ustore.mem
cpu.v
Memory
Controller
IUNIT
EUNIT
Micro-
Store
Main Memory
TTY
tty.v
tty.tcl
VPD

## Slide 10: Drink Machine VPD
VPD Implementer
  Writes Tcl script implementing behavior.
  Writes Verilog stub-module encapsulating interface.
VPD Client
  Loads library with desired VPD.
  Creates one or more instances.
  Creates control logic.
User Circuit
Drink Machine Verilog Interface
Verilog-Side API
Simulator
TkGate Tcl Code
Drink Machine Tcl/Tk Interface
Tcl-Side API
User Interface
Pipe/socket

## Slide 11: Drink Machine Window
Drag and drop coins/bills to insert into machine.
Push buttons to make drink selections.
User circuit can activate “empty” and “no change” lights.
Internal view shows inserted coins/bills and drink columns

## Slide 12: Including a VPD in the User’s Design
Users interact with VPD as a normal module.
  Create one or more instances in user module.
  Interact though ports on VPD module.
Users can create multiple instances of a VPD.
  Each VPD is assigned a unique instance name from the Verilog hierarchy.
  Verilog instance name is used as VPD instance identifier in the Tcl script.
module top;
wire [5:0] PRESS1, PRESS2;
wire NOCHG1, NOCHG2;
...
drinkmachine dm1(..., PRESS1, NOCHG1, ...);
drinkmachine dm2(..., PRESS2, NOCHG2, ...);
...
endmodule
top.dm1
top.dm2

## Slide 13: Example Interaction
CHGQ
CHGACK
25
18
10
9
19
Wait for CHGACK to go low indicating it is OK to dispense change.
Assert CHGQ to tell drink machine to give a quarter in change.
Wait for CHGACK to go high indicating change operation has completed.
Clear CHGQ to complete transaction.
CHGACK goes low to acknowledge transaction completion.
Command sent to Tcl-side of VPD to update display

## Slide 14: Named Channels
Created dynamically as needed.
Implemented as queue that can be accessed from both Tcl and Verilog.
Objects on queue are arbitrary bit-sized values.
One named channel used for each signal passing between Tcl-Side and Verilog-Side of implementation.
$tkg$send
VPD::insignal
“top.dm1.CHGACK”
VPD::outsignal
$tkg$recv
“top.dm1.CHGQ”
Verilog-Side
Tcl-Side

## Slide 15: Tcl-Side API Highlights
VPD::register name
VPD::newtoplevel –title title –shutdowncommand command
VPD::outsignal chan variable
VPD::insignal chan [-variable variable][-command command]
Register name as a virtual peripheral device. Registered VPDs can be posted using the $tkg$post() task from Verilog.
Create a new top-level window for use as a VPD. Top-level windows created with this command will be given the specified title. When simulation mode is terminated, the window will be destroyed and the specified shut-down command will be invoked.
Associate an input channel with a Tcl variable and/or command. When data from the simulator is sent on the named channel, the registered Tcl variable will be set and/or the registered command will be called.
Associate an output channel with a Tcl variable. When a value is assigned to the registered variable, data will be sent

## Slide 16: Verilog-Side API Highlights
$tkg$exec(format, p1, ..., pn)
$tkg$post(vpdname, instname, p1, ..., pn)
$tkg$send(name, data)
$tkg$recv(name)
Construct a Tcl command and execute it. Executed commands are subject to the current security policy.
Call the “post” procedure for a registered VPD passing the specified argument list. The instance name and one or more optional parameters are passed as arguments to the “vpdname::post” command.
Send data on a named channel.
Receive data on a named channel. Blocks if no data is available in the queue.

## Slide 17: Drink Machine VPD Overview
VPD::register DrinkMachine
namespace eval DrinkMachine {
variable dm_w
variable CHGACK
...
proc post {name} {
...
}
}
Name of VPD. The VPD should be registered with tkgate, and Tcl code for the VPD should be defined within a namespace.
Array of top-level windows indexed by instance name.
Instance name of VPD passed as parameter.
Array with current state of the “change acknowledge” signal for each VPD instance.
Tcl procedure to create an instance of the drink machine VPD.

## Slide 18: “post” Proceedure (Creating Window)
set dm_w($name) [VPD::newtoplevel \
-title "Vending Machine $name" \
-shutdowncommand "DrinkMachine::unpost $name"]
Variable to store name of window for VPD instance
VPD instance name (e.g., “top.dm1”)
Window for VPD will be labeled “Vending Machine top.dm1”
The “unpost” procedure for this VPD will be invoked when the simulation is terminated.

## Slide 19: “post” Procedure (Registering Output Signals)
VPD::outsignal $name.CHGACK DrinkMachine::CHGACK($name)
set CHGACK($name) 0
Register a signal from the Tcl-side to the Verilog-side.
Named channel to use (e.g. “top.dm1.CHGACK”)
Tcl variable to attach to the named channel.
Send a “0” to the Verilog-side of the implementation.

## Slide 20: “post” Procedure (Registering Input Signals)
VPD::insignal $name.CHGQ \
-command DrinkMachine::dispenseQuarter \
-variable DrinkMachine::CHGQ($name)
-format %d
Register a signal from the Verilog-side to the Tcl-side.
Named channel to use (e.g. “top.dm1.CHGQ”)
Tcl procedure to call when data is received on this channel.
Format in which Verilog should data should be passed to procedure or variable.
Variable to assign when data is received on this channel.

## Slide 21: Verilog-Side VPD Definition
module drinkmachine(..., CHGQ, CHGACK, ...);
output CHGACK;
reg CHGACK;
input CHGQ;
initial
$tkg$post("DrinkMachine","%m");
always #10
CHGACK = $tkg$recv("%m.CHGACK");
always @ (CHGQ)
$tkg$send("%m.CHGQ",CHGQ);
...
endmodule
Module port declarations
Port type declarations
Create VPD window
Receive data from Tcl-side
Send data to Tcl-side

## Slide 22: Initialization
initial
$tkg$post("DrinkMachine","%m");
Verilog “execute once” statement.
Type name of VPD to post.
Name of VPD instance.
“%m” replace with instance name (e.g., “top.dm1”).
Simulator
Interface
“go (start simulation)”
“post DrinkMachine top.dm1”
VPD::newtoplevel

## Slide 23: Tcl->Verilog Dataflow
always #10
CHGACK = $tkg$recv("%m.CHGACK");
Simulator
Interface
“$send top.dm1.CHGACK 1”
Verilog “infinite loop” statement.
Delay
Named channel to read.
CHGACK
Verilog signal to update.
10
set CHGACK(top.dm1) 1

## Slide 24: Verilog->Tcl Dataflow
always @(CHGQ)
$tkg$send("%m.CHGQ",CHGQ);
Named channel to use
Verilog signal to send
Simulator
Interface
Verilog “infinite loop” statement.
Block until signal changes.
CHGQ
“send top.dm1.CHGQ 1”
25
DrinkMachine::dispenseQuarter top.dm1

## Slide 25: Alternate Dataflow Styles
Simulator
TX
CTS
RD
41
always @(posedge TX)
if (CTS)
$tkg$send("%m.DATA",TD);
On a positive edge of TX…
… if the CTS signal is asserted …
… send the data in TD.
Interface
“send top.tty.DATA 8’h42”
42
B
A
$tty_w($name).text insert insert “B”

## Slide 26: TkGate Architecture
User Tcl Commands
Tk_Main
Named Channels
Circuit State
Byte-code
Thread Execution
Simulator
pipe
Simulator Interface
Edit Window Handler
Command Processing
Design Data
user.v
Verilog Compiler
Event Handler
Input/
Output
Interface
temp.v
libs.v
libs.v
libs.v
libs.v
libs.v
vpd.v
fileevent
Core TkGate Tcl Files
System and User-Defined VPD Files
User Design Data
System and User Library Data
System and User VPD Stub Modules
C
Tcl/Tk
GUI Handler
VPDs
bind
bind
Verilog Parser/
Generator
Tcl_Eval
libs.v
libs.v
tkgate.tcl
libs.v
libs.v
vpd.tcl

## Slide 27: Conclusion
Virtual Peripheral Devices
  Mechanism to create interactive devices.
  Devices appear as ordinary module to user design.
  Signals on Verilog module translated into Tcl commands in interface.
  Named channels used to communicate between Tcl and Verilog side.
Implementation
  Tcl/Tk Graphical Interface
    Defined in unique namespace.
    Provide “post” method to create window.
    Bind Tcl variables and commands to named channels.
  Verilog Stub Module
    Use Verilog “initial” to invoked the VPD “post” command.
    Use Verilog “always” to link Verilog variables to Tcl variables.
    More complex multi-variable interactions can also be implemented.
http://www.tkgate.org

## Slide 28: TkGate Architecture
libs.v
libs.v
libs.v
temp.v
C code
C-side
Tck/Tk-side
libs.v
libs.v
user.v
libs.v
libs.v
core script files
libs.v
libs.v
VPD script files

## Slide 29: Drink Machine VPD
VPD Implementer
  Writes Tcl script implementing behavior.
  Writes Verilog stub-module encapsulating interface.
VPD Client
  Loads library with desired VPD.
  Creates one or more instances.
  Creates control logic.
User Circuit
Drink Machine Verilog Interface
Verilog-Side API
Simulator
TkGate Tcl Code
Drink Machine Tcl/Tk Interface
Tcl-Side API
User Interface
Pipe/socket

## Slide 30: TTY Virtual Peripheral Device
main.mem
ustore.mem
cpu.v
Memory
Controller
IUNIT
EUNIT
Micro-
Store
Main Memory
TTY
tty.v
tty.tcl
VPD

## Slide 31: TkGate Architecture
Event Handler
Verilog Compiler
Named Channels
Circuit State
Verilog Byte-code
Thread Execution
Simulator
Interface
Input/
Output
pipe
Simulator Command
Processing
Main Window Handler
TK_Main
Command Processing
libs.v
libs.v
vpd.tcl
libs.v
libs.v
tkgate.tcl
Design Data
User Commands
Interface Handler
libs.v
libs.v
libs.v
libs.v
libs.v
vpd.v
user.v
temp.v
Verilog Parser/
Generator