## Slide 1: Pulling Out All the Stops
Application of Tcl user extensions in a high performance multi-threaded electronic design application
by Phil Brooks

## Slide 2: Calibre Design Verification
Integrated Circuit Design
Geometric Analysis Tool

## Slide 3: Layout vs. Schematic (LVS)
Schematic – logical design of a circuit
Layout – physical design of a circuit
LVS makes sure Layout and Schematic designs describe the same circuit by comparing them

## Slide 4: Device Recognition
Device Recognition allows the user to turn geometric shapes from the layout into logical devices:

## Slide 6: Built-in Script Language
Very Simple
Very High Performance

## Slide 7: Built-in Script Language
byte compiled interpreted user program
program configures data collection before execution starts
Very limited capabilities
  no loops, no allocation
  just data collection, arithmetic, and conditionals

## Slide 8: Built-in Script Language
Data and temporary variables are pre-allocated
Byte code runs for each device that is recognized

## Slide 9: Built-in Script Language
DEVICE MP PGATE PGATE(G) SD(S) SD(D) DIFF
[
property w, l
w = 0.5 * ( perim_co( S, G )
+ perim_in( S, G )
+ perim_co( D, G )
+ perim_in( D, G ) )
l = area( G ) / w
if( ( bends( G ) != 0 ))
{
if( w > l )
w = w – 0.5 * bends( G ) * l
else l = l – 0.5 * bends( G ) * w
}
]

## Slide 10: Built-in Script Language
Byte Code
ADD temp3 perim_co(S,G) perim_in(S,G)
ADD temp2 temp3 perim_co(D,G)
ADD temp1 temp2 perim_in(D,G)
MUL w 0.5 temp1
DIV l area(G) w
NE bends(G) 0 [31] [70]
GT w l [37] [55]
MUL temp2 0.5 bends(G)
MUL temp1 temp2 l
SUB w w temp1
GOTO [70]
MUL temp2 0.5 bends(G)
MUL temp1 temp2 w
SUB l l temp1
HALT
Variable Name Value
w 0.0
l 0.0
temp1 0.0
temp2 0.0
temp3 0.0
perim_co(S,G) 4
perim_in(S,G) 6
perim_co(D,G) 4
perim_in(D,G) 6
area(G) 12
bends(G) 2

## Slide 11: Reaching the Limits of Built-in
A1,P1
A2,P2
A4,P4
A3,P3
L1
L2
L3
W1
W2
W3
S2’
S1
S3’
S4’
S5
S6
S3’’
W2’’
W2’
W2’”
W1’
W1’’
S2”
S4”
Enclosure Functions

## Slide 12: Reaching the Limits of Built-in
Complex measurements
No simple number representation
Summation capability required

## Slide 13: Reaching the Limits of Built-in
  DEVICE MP PGATE PGATE(G) SD(S) SD(D) DIFF
  [
  property W, L, SEFFA
  W = 0.5 * ( perim_co(S,G) +
  perim_in(S,G) + perim_co(D,G)
  + perim_in(D,G) )
  L = area(G) / W
  if( ( bends(G) != 0 ))
  {
  if( W > L )
  W = W - 0.5 * bends(G) * L
  else L = L - 0.5 * bends(G) * W
  }
  S = ENC_PER (PGATE, DIFF, SD, 25)
  SEFFA = W / SUM(S::W / (S::A + 0.5*L) ) - 0.5*L
  ]

## Slide 14: Reaching the Limits of Built-in
Sum functionality satisfied specific requirements
Soon a more general solution was needed
  min/max
  arbitrary calculations on array elements
  a more complex measurement array
    Multi Finger Enclosure measurements

## Slide 15: Scripting Language Requirements
Describe data collection prior to execution
  Built-in language data retrieval function configures data collection algorithms
Leverage existing Built-in script engine
  Customers have extensive existing usage
  Built-in engine has 31 data collection routines
Get data collected to the script
Get calculated results back
Overall Performance can’t slow down too much

## Slide 16: Why Tcl?
Calibre already has Tcl interfaces inside our geometric manipulation language

## Slide 17: How Tcl?
Add a function interface to the Built-in language – TVF_NUMERIC_FUNCTION (TVF_NUM_FUN for short)
Allows calling a Tcl Function from within the Built-in language

## Slide 18: How Tcl?
DEVICE MP PGATE PGATE(G) SD(S) SD(D) DIFF
[
property W, L, SEFFA
W = 0.5 * ( perim_co(S,G) +
perim_in(S,G) + perim_co(D,G)
+ perim_in(D,G) )
L = area(G) / W
if( ( bends(G) != 0 ))
{
if( W > L )
W = W - 0.5 * bends(G) * L
else L = L - 0.5 * bends(G) * W
}
S = ENC_PER (PGATE, DIFF, SD, 25)
SEFFA = TVF_NUM_FUN (
"calc_eff_a",
"device_func ", S, W, L
)
]

## Slide 19: How Tcl?
TVF FUNCTION device_func [/*
proc calc_eff_a { enc W L } {
... tcl code ...
}
*/]

## Slide 20: Requirements Check
Describe data collection before script runs
  Existing built-in script engine still provides the data collection functions
Leverage existing script engine and customer scripts
  Add Tcl calls to Existing built-in scripts
Get data collected to Tcl
  Function call arguments
Get data calculations back to Calibre
  Return values of Tcl functions called
Overall Performance goal

## Slide 21: Performance Testing
Test Circuits: Emphasize scripting language performance (not a real world test case)
  500,000 devices that run through the calculation script
    3 Builtin->Tcl calls for each device (1.5 million total)
    10 Tcl->Calibre object callbacks (5 million total)
  Realistic Device Calculations
  Partitions into 18 equal partitions for Multi-Threaded execution
  Can be expressed as Tcl function or Built-In SUM

## Slide 22: Efficiently Calling Tcl
What call interface to choose:
  Tcl_Eval
  Tcl_EvalEx
  Tcl_EvalObjEx
  Tcl_EvalObjv

## Slide 23: Efficiently Calling Tcl

## Slide 24: Efficiently Calling Tcl

## Slide 25: Efficiently Calling Tcl

## Slide 26: Efficiently Calling Tcl
Use of Tcl_EvalObjEx didn’t differ significantly from Tcl_EvalObjv
Argument Handling
  Set up as much as possible before execution
  Data passed through objects (Tcl_CreateObjCommand) to avoid construction of argument objects

## Slide 27: Getting Back to C++
Data is passed back through a Tcl_DoubleObj set as the “result”
Tcl handles the result objects efficiently

## Slide 28: Writing Efficient Tcl
Beware the use of expr without {}
changing expr { ... } to expr ...
  reduced performance by 300%

## Slide 29: Writing Efficient Tcl
Consider object interfaces that do the bookkeeping operations:
  set slice_count [ $enc slice_count ]
  for { set i 0 } { $i<$slice_count } { incr i } {
  # slice specific code here uses index $i to access data
  # from the $enc command object by passing it in as an argument
  }

## Slide 30: Writing Efficient Tcl
Consider this interface where the $enc object performs index calculations
  set i [ $enc first_slice ]
  while { $i > 0 } {
  # slice specific code here index is implicit $enc will
  # access data from the current array slice.
  set i [ $enc next_slice ]
  }
Or, if you want to get fancy:
  $rtval = $enc eval {
  # some sort of code that executes once for each slice
  }

## Slide 31: Writing Efficient Tcl

## Slide 32: Threads
Data is partitioned for parallel execution
  Each thread recognizes devices independently
  Each thread runs its own copy of the built-in language engine
How do threads perform with Tcl?
Better to use MT Tcl or Single Threaded Tcl?

## Slide 33: Threads

## Slide 34: Final Performance Numbers
  Real chips showed no increase in required CPU time for Device Recognition