## Slide 1: LCCS
A Pure Tcl/Tk Train Traffic Supervision System

## Slide 2: Agenda
About LCCS
Train Traffic Supervision: what they are and how they look like.
The LCCS implementation
Reading synoptic description and configuration
Examples
Reflection, code generation
The Tcl/Tk features I like most
Questions?

## Slide 3: About LCCS
Is a local train traffic supervision software
  LCCS stands for Local Control Computer Software
Was developed by J.Lima and J.Rocha to the Lisbon Underground Train Company
  Demonstrate the feasibility of the entire Train Trafic supervision and control software using Tcl/Tk
  Replace the obsolete system just being installed
The idea was supported by the engineering team and by the operators
However, it was rejected by the managment

## Slide 4: For what is used for?
Supervise the railway state
Interact at the operational level: granting or defering a train departure
Redefine the itineraires (source, destination and path)
Manualy conducting manouvers*
Perform abnormal condition recovering procedures
  The driver crossed the boundary of a forbiden zone
  A train is malfunctioning

## Slide 5: How they look like?
LCCs are based on Workstations or PCs. However, they work much like embedded systems
  We don’t want operators playing solitaire!
  X11 session will launch a single full screen application (no window manager)
  No further control is granted to the operator
  The system must be capable of recovering from software errors – should have no history...

## Slide 6: One word about safety
In railway systems safety and functionality are handled separately:
  The operational/supervision software handles functionality
  The PLC hardware handles the all safety issues

## Slide 8: Implementation
Original Idea
  Tcl/Tk GUI
  Dedicated canvas for the synoptic
  Extensions for communication with the PLC
Everything coded in Tcl
  The synoptic; the communication modules
  The configuration can be TCL as well
  Even the communication protocols are forms of TCL

## Slide 9: The Tcl Orgy
Tcl config
files
programs coded
in bare tcl
messages
exchanged
between processes
are in TCL
IO is also
a form of tcl

## Slide 10: Reading synoptic and configuration The importance of safe interpreters
Without safe interpreters
  Applications which source configuration files can not be trusted to run in a realistic scenarios
  We would have to write our own input processors
With safe interpreters
  Implementing a specialised parser is straightforward
proc Config::Colors {file} {
proc set_color { object color } {
global COLORS
set object [string tolower $object]
set COLORS($object) $color
}
set parser [interp create -safe]
$parser hide set
$parser alias set Config::set_color
SafeSource $parser $file
interp delete $parser
rename set_color {}
}

## Slide 11: Initialization
#
# Load The Configuration
#
Config::Colors [file join $ETC Colors]
Config::Scales [file join $ETC Scales]
Config::LanguageStrings [file join $ETC Language]
#
# Load Synoptic
#
Config::Synoptic $canvas [file join $ETC global Synoptic]
#

## Slide 12: Synoptic description files
# Railway synoptic
include global/Segments
include global/Scales
# Rail circuits
# id segments variable label
cdv C1-AM {seg1} A001 "C1"
cdv C3-AM {seg3} A003 "C3"
cdv C5-AM {seg5a seg5b} A005 "C5"
cdv C7-AM {seg7a seg7b} A007 "C7"
cdv C9-AM {seg9} A009 "C9"
cdv C11-AM {seg11a seg11b} A012 "C11"
cdv C13-AM {seg13} A013 "C12"
# Trafic lights
# id coordinates anchor variable label
s2 M1-AM {3500 8700} {top left} A014 "M1"
s2 M3-AM {9000 8700} {top right} A015 "M3"
sb SB-AM {11400 8700} {top left} B016 "SB"
s4 S5-AM {11000 8700} {top left} A016 "S5"
#
# Via ascendente
#
seg seg1 {{2000 8500} {3500 8500}}
seg seg3 {{3562 8500} {5000 8500}}
seg seg5a {{5062 8500} {7000 8500}}
seg seg5b {{7000 8500} {6500 8500} {6040 8040}}
seg seg7a {{7062 8500} {9000 8500}}
seg seg7b {{7062 8500} {7500 8500} {7960 8040}}
seg seg9 {{9062 8500} {11000 8500}}
seg seg11a {{11062 8500} {13000 8500}}
seg seg11b {{11062 8500} {11500 8500} {11960 8040}}
seg seg13 {{13062 8500} {14500 8500}}
seg seg101 {{14562 8500} {16000 8500}}
#
# Scales file
#
Xscale 0.04
Yscale -0.04

## Slide 13: Configuration files
# Valid color names:BGROUND FGROUND CDVFREE CDVOCUP
# CAISCOLOR TEXTCOLOR WARNCOLOR ERROCOLOR CANLCOLOR
# OKCOLOR INATCOLOR BLUNAR VIOLET ROUGE VERT
# Synoptic colors
set CDVFREE "#fffff916dced"
set CDVOCUP "#f80f13f84000"
set BGROUND "#000000000000"
set FGROUND "#dceddceddced"
set CAISCOLOR "#a6a7a6a7a6a7"
set TEXTCOLOR "#ffffffffffff"
set WARNCOLOR "#ffc0ffff845a"
set ERROCOLOR "#f80f14183fdd"
set CANLCOLOR "#f80f14183fdd"
set OKCOLOR "#4854cc074320"
set INATCOLOR "#edededededed"
# Trafic light colors
set WLUNAR "#fffffa5cec49"
set VIOLET "#950b0000d3b5"
set RED "#ffff0000424e"
set GREEN "#0000efde0000"
# Language File
#
set LANGUAGE portuguese
# Strings.portuguese File
#
set AM2 "ALAMEDA 2"
set OL "OLAIAS"
set BV "BELA VISTA"
set CH "CHELAS"
set CR "CABO RUIVO"
set OS "OLIVAIS SUL"
set OR "ORIENTE“
set OK "Confirmar"
set CANCEL "Cancelar"
set EXIT "Sair"
set CDV "CDV"
set COMC "Comando central"
set COML "Comando local"
set IT "Itinerários"
set IA "Itinerários automáticos"
set IP "Itinerários permanentes"
set BS "Bloqueio de saída"
set COMERR "Erro de comunicação com o MicroLok"

## Slide 14: Reflection, code generation
The synoptic is generated together with the code which will implement its functionality
  For the small synoptic presented here >50% of automaticaly generated code
  For large synoptics can go up to ~99%

## Slide 15: Code generation How hard is to write code?
Application
code
code generating code
Configuration
dinamicaly generated code
Hardness scale
Hardest
softest

## Slide 16: Cool Tcl/Tk features
Tcl fine control of its slave interpreters
Code and data share the same representation
Tk supports complex GUIs and megawidgets as well as the simplest, and ugliest conceivable GUIs

## Slide 17
Questions?